## Slide 1: Gesture controlled gaming glove
Embedded Systems

## Slide 2: Embedded systems Dr Musa ALYAMAN
Asya Samer
Dana Abu Al Ruz
Ethar Al Salameh
Layla Al Laham
Jana Saleh Godieh
Leen Masarweh
0222211
0224982
0222126
0223839
0223457
0222209

## Slide 3: Presentation outline
Level 1
introduction
Level 5
connections
Level 3
Flowchart
Level 4
Algorithms
Hardware
Level 2
Level 6
Sketch
Level 7
Conclusion
Final boss
Testing

## Slide 4: Gesture controlled gaming glove 1. Introduction
A gaming glove that captures simple hand
gestures and uses them to explore and
control games for a more immersive and
enjoyable gaming experience

## Slide 5: Project motivation
Make gaming accessible for users with amputations, disability and limited mobility
Create a fun, intuitive control system using gestures
Affordable alternative to expensive VR systems

## Slide 6: 2. Hardware ESP32 Microcontroller
This board is the brain of the system.
It reads data from the sensors and
sends it to the laptop via Wi-Fi using
UDP protocol. We chose the ESP32
because it’s powerful, has great
connectivity options, and works well
in small wearable setups.

## Slide 7: 2. Hardware MPU6050
This small sensor combines an accelerometer and a gyroscope, allowing us to detect movement and direction

## Slide 8: Flex sensor 2. Hardware
The flex sensor, which is strapped to the index finger using a silicone glove, gives analog readings to the ESP32.

## Slide 9: 3.Flowchart
Power On and System Initialization Sensor Data Acquisition
Data Transmission using UDP
Data Processing in Python Script
Gesture-to-Action Mapping
Unity Game Control
Visual and Audio Feedback

## Slide 10: 4.Description of algorithms that controls the systems operation
Continuous Loop:
The system runs in a continuous loop:
Sensors continue to receive new input.
Data is sent to the laptop.
Python updates a txt file read by the Unity game code
The loop ensures the player gestures are consistently updated on the game without delays.

## Slide 11: Description of algorithms that controls the systems operation
Power On and System Initialization
The system runs on a 7.4V Li-ion battery, which is regulated down to 5V by a voltage regulator to supply the ESP32.
Once powered, the ESP32 initializes the necessary GPIOs and I2C communication with mounted sensors (flex sensor and MPU6050). It also establishes a UDP connection to the laptop.

## Slide 12: Description of algorithms that controls the systems operation
Sensor Data Acquisition:
The flex sensor, which is strapped to the index finger using a silicone glove, gives analog readings to the ESP32.
The MPU6050, contained in a 3D-printed case in the glove's rear, gives the gyroscope readings (movement Y-axis, rotation Z-axis) constantly through I2C.
The ESP32 reads these values in real time and prepares them to send.

## Slide 13: Description of algorithms that controls the systems operation
Data Transmission using UDP:
ESP32 transmits the sensor readings collected wirelessly to the laptop using UDP protocol. This ensures low-latency transmission for fast gameplay.

## Slide 14: Description of algorithms that controls the systems operation
Data Processing in Python Script:
The laptop hosts a Python script that reads serial output and writes it on a txt file that the Unity game code checks :
If the value of the flex sensor goes over a shooting threshold.
If MPU6050 values indicate forward/backward movement or left/right turning.

## Slide 15: Description of algorithms that controls the systems operation
Gesture-to-Action Mapping:
The unity code interprets the sensor readings to respective game actions:
Finger fold (flex sensor) → shoots the weapon.
Move forward/backward (MPU6050 Y-axis) → moves the player forward/backward.
Turn left/right (MPU6050 Z-axis) → turns the direction of the player.
These commands are communicated to the Unity game environment.

## Slide 16: Description of algorithms that controls the systems operation
Visual and Audio Feedback:
The laptop screen (visual actuator) displays the game, and the laptop speakers (audio actuator) provide sound effects such as footsteps, guns, or zombie screams. These feedbacks are a result of the player's actions and maintain the player engaged.

## Slide 17: 5.Connections
Component | Pin on Component | Connects To ESP32 Pin
MPU-6050 | VCC | 3.3v
 | GND | GND
 | SCL | GPIO 22
 | SDA | GPIO 21

## Slide 18: Connections
Component | Pin on Component | Connects To ESP32 Pin
Flex sensor | One side | 3.3v
 | Other side | GND through resistor
 | midpoint | GPIO 34

## Slide 19: 6.Conclusion
In this project, we designed and built a gaming gesture glove that lets players control a game using hand movements. We tested it on a zombie-killer game to show how it works in a real gaming situation. While the main goal was to make gameplay more fun and interactive, our project also has the potential to make an economic impact.

## Slide 20: 7.Expected impact and future opportunities
Award 1
A Cheaper Option for Motion Control
Award 2
New Opportunities in the Gaming Market
Award 3
Rehabilitation
Semulation training
Education
Award 4
Encouraging innovation and tech skills

## Slide 21: Testing!